## Slide 1: Internet of Things Workshop
Build your own device!

## Slide 2: Agenda
Goal
Device
Sensor
Electrical Engineering Basics
Software

## Slide 3: Goal

## Slide 4: Real goal
Create an IoT device
Program an IoT device
Send data to the cloud secure
Process data
Store data
Analyze data
Display information

## Slide 5: Device - WeMos D1 Mini
http://www.wemos.cc/Products/d1_mini.html

## Slide 6: Sensor - Maxim DS18B20

## Slide 7: NC, GND, VCC

## Slide 8: ???

## Slide 9: Pull up, Pull down, DS18B20 wiring

## Slide 10: Device - WeMos D1 Mini
http://www.wemos.cc/Products/d1_mini.html

## Slide 11: Ohm's law
V=I*R
I = V/R
R = V/I
V = Voltage
I = Current (Ampere)
R = Resistance (Ohm)
Power = V*I (Watt) => 16A * 220V = 3520Watt

## Slide 12: LED Resistor
Max Current = 20mA
Voltage Drop = 1.9V
Which resister is required if my development board supplies 3.3V?
3.3V – 1.9V = 1.4V
R = V/I = 1.4/0.020 = 70 => 75 Ohm resistor

## Slide 13: Arduino
https://www.arduino.cc/
The go to tool to create small solution for devices/boards
Board manager
Library manager

## Slide 14: Visual Studio
https://www.visualstudio.com/
The tool for large/complex projects
If you want to develop for devices install with C++

## Slide 15: Visual Micro
The glue between Arduino and Visual Studio
Allows for debugging!

## Slide 16: Labs
Lab 1
  Wiring your device
  Configure your device
Lab 2
  Configure your evironment
  Upload the latest code